FLAIL MOWER

#### INSTRUCTIONS

###### FL100/FL125/FL150

FL-100/125/150 Flail Mower Instructions

# SAFETY INSTRUCTIONS

Do not attempt to operate the mower until you have read the operator’s manual and all the safety signs on the mower.

NOTE: The words Danger, Warning or Caution on the safety signs indicate a hazard or unsafe practice, which could result in injury or death if proper precautions are not taken.

Do not attempt any unauthorized modifications to the mower as this could affect the function or the safety of the mower.

# OPERATING SAFETY

1. Keep all safety signs clean and legible at all times. Replace damaged or missing safety signs.

2. Ensure all shields are in place and in good condition before operating.

3. Ensure everyone is clear of the area before operating.

4. Never start or operate the mower except from the operator’s station on the power unit.

5. Do not permit riders.

6. Stop engine, set brake, remove key and wait for all moving parts to stop before servicing, adjusting, repairing and unplugging.

7. Never operate over 540 rpm PTO speed.

8. Inspect and clean the cutting area before cutting.

9. Never operate the mower in the raised position.

10. Do not wear loose fitting clothing during operation.

11. Keep hands, feet, clothing and hair away from moving parts.

12. Keep all bystanders away from the unit when it is operating.

13. Check to see that all controls are in neutral before starting the tractor.

# TRANSPORT SAFETY

- Do not transport on a public road without a slow moving vehicle sign and flashers on the tractor.

2. Never have the mower in operation during transport.

3. Travel speed with a raised mower should be slow enough to maintain stability of the tractor.

# SERVICE AND MAINTENANCE SAFETY

1. Stop engine, set brake, remove key and wait for all moving parts to stop before servicing, adjusting, repairing or unplugging.

2. Block up before working beneath unit.

3. Replace all shields removed during servicing before operating.

4. Use heavy leather gloves to handle sharp blades.

The safety signs used on the mower must be in well condition and be read clearly.

Replace safety sign immediately if it becomes damaged, torn or illegible.

# OPERATING INSTRUCTIONS

The Flail Mower is designed to be used on a tractor with a standard category 1 three-point hitch. Never to use the PTO rate over 540rpm . Using excessive power will shorten the life of the drive train components.

# CONNECTING TO TRACTOR

Park the mower and tractor on a level dry area free of debris and foreign objects.

1. Slowly back the tractor up to the mower.

2. Adjust the three-point arms to align with the mower lift pins.

3. Stop the tractor, set the parking brake and remove the ignition key before mounting.

4. With the engine on the tractor shut off, attach the PTO shaft. Both ends of the PTO have a standard 6-spline end with a spring-loaded locking collar.

Turn the round collar at the ends of the PTO clockwise to slide onto the spline shafts.  Always check to see that both ends of the PTO shaft are securely attached every time the mower is used. This should always be done with the tractor engine shut off. Attach the safety chains supplied with the PTO shaft, allowing sufficient slack for the driveline during turns and operation.

NOTE: At least one third of the telescoping length of the PTO should overlap when the mower is in operation.

5. Attach the top link on the tractor to the link pin assembled in the upper lift pin bracket . Adjust the turnbuckle on the tractor top link so that the upper lift bracket hangs straight down with the tractor and mower both on level ground.

# FIELD USE PREPARATION

1. Park the machine on hard level ground with the mower slightly raised.

- Adjust the sway blocks or chains on the tractor so the mower is centered between the rear wheels.

3. Adjust the three-point arms to level the mower side to side.

4. Adjust the turnbuckle on the top of the three-point hitch arms to level the mower front and back.

5. Adjust the cutting height using the wheel spacers on the wheel yokes. The spacers should be set at the same height on all four wheels.

6. Check the oil level in the gearbox and add as required .

7. Grease spindle assembly, wheel bearings, wheel pivots and the PTO shaft .

8. Check tightness of belts, bolts and other hardware .

9. Check blades to see if they are damaged. Sharpen or replace blades if necessary. Check that blade bolts are tight.

10. Clear the working area of foreign objects and check that all bystanders are standing clear before starting.

11. Start the tractor with the mower resting on the ground on all four wheels.

12. Slowly engage the PTO and bring the PTO speed up to 540 rpm for cutting.

# FIELD OPERATION

1. The PTO must run at the full 540 rpm for a good cut. Slower speeds or double cutting could be required for very high grass.

3. Use a higher blade setting for rough areas to prevent scalping of the surface.

4. Always cut counter-clockwise so grass clippings are thrown on the grass already cut. This saves power and wear on the blades.

5. Sharpen blades if grass tears instead of cutting cleanly.

6. Slow down when cutting corners. Turning too sharply on corners can leave a small strip of grass uncut.

# DISCONNECTING FROM TRACTOR

1. Park on a firm level area and clean the mower.

2. Lower the mower until the load is off the hitch arms.

3. Disconnect the hitch arms and the PTO shaft.

4. Cover the mower for storage to prevent rust.

# MAINTENANCE

1. GEARBOX: The gearbox should be filled with SAE 90 oil to the bottom of level plug . Check the mower before using and at regular intervals (approx. every 40 hours). See that this oil level is maintained.

2. Lubrication: all rotor drum, roller,bearings should be lubricated  to ensure long time life .

Driveline inner tube,u-joint should be lubricated every 8-16 hours.

3. SHIELDING: Always keep all shielding in place and repair or replace if damaged.

4. BLADES: When replacing or grinding blades, all three blades must be replaced or reground at the same time to maintain the proper balance in the cutting unit. Block up the mower securely before attempting to remove the blades. Use heavy leather gloves to handle the blades. Be sure to tighten bolt and lock securely when replacing blades.

5.BELTS: Remove the belt guards to check belt tightness. The center of the belt span should deflect about 10mm with nominal pressure. If the belts slip or are too loose, the bolts holding the gearbox must be loosened.

Use the threaded tightener rod on the gearbox mount to tighten the belts. Lock the rod in place and re-tighten the gearbox bolts when the belts are properly tightened. Replace belt guards. Changing belts follows the same procedure as given in the preceding paragraph, except you will have to loosen the belts further to remove them.

NOTE: Belts should always be replaced in matched sets.

### FLAIL MOWER PARTS LIST

FL-100/125/150 Flail Mower Parts List

| ITEM | PART # | DESCRIPTION |
| --- | --- | --- |
| 1 | GB5782 | Bolt M10x130 |
| 2 | FL100.10.001 | FL100 Gearbox Assembly |
|  | FL125.10.001 | FL125 Gearbox Assembly |
|  | FL150.10.001 | FL150 Gearbox Assembly |
| 3 | FL100.10.101 | Gearbox support |
| 4 | GB97.1 | Plain washer 10 |
| 5 | GB93 | Lock washer 10 |
| 6 | GB6170 | Nut M10 |
| 7 | GB5783 | Bolt M10x25 |
| 8 | GB6170 | Nut M12 |
| 9 | FL100.10.010 | Mounting plate |
| 10 | GB5783 | Bolt M10x35 |
| 11 | FL100.10.102 | Pulley |
| 12 | FL100.10.103 | Outer bushing |
| 13 | FL100.10.104 | Inner bushing |
| 14 | GB70 | Screw M6x25 |
| 15 | GB276 | Bearing 208 |
| 16 | GB5783 | Bolt M10x25 |
| 17 | FL100.10.105 | Right flange |
| 18 | FL100.10.011 | FL100 Blade shaft |
|  | FL125.10.011 | FL125 Blade shaft |
|  | FL150.10.011 | FL150 Blade shaft |
| 19 | GB5782 | M12x45 |
| 20 | FL100.10.106 | Blade |
| 21 | GB6170 | Lock nut M12 |
| 22 | FL100.10.107 | Driven Pulley |
| 23 | GB893 | Snap ring 80 |
| 24 | FL100.10.108 | Left flange |
| 25 | FL100.10.109 | Lift pin |
| 26 | GB93 | Lock washer 22 |
| 27 | GB6170 | Nut M22x1.5 |
| 28 | GB6170 | Plain washer 10 |
| 29 | GB91 | Cotter 3x15 |
| 30 | FL100.10.110 | FL100 Chip bar |
|  | FL125.10.110 | FL125 Chip bar |
|  | FL150.10.110 | FL150 Chip bar |
| 31 | FL100.10.111 | Chip |
| 32 | FL100.10.012 | FL100 Deck |
|  |  | FL125 Deck |
|  |  | FL150 Deck |
| 33 | GB5782 | Bolt M16x140 |
| 34 | FL100.10.013 | Upper lift connector |
| 35 | GB93 | Lock washer 16 |
| 36 | GB6170 | Nut M16 |
| 37 | FL100.10.112 | Lift bar |
| 38 | GB5783 | Bolt M16x45 |
| 39 | GB93 | Lock washer 16 |
| 40 | GB6170 | Nut M16 |
| 41 | FL100.10.014 | FL100 Roller support /right |
|  | FL125.10.014 | FL125 Roller support /right |
|  | FL150.10.014 | FL150 Roller support /right |
| 42 | FL100.10.015 | FL100 Scraper |
|  | FL125.10.015 | FL125 Scraper |
|  | FL150.10.015 | FL150 Scraper |
| 43 | FL100.10.016 | FL100 Roller |
|  | FL125.10.016 | FL125 Roller |
|  | FL150.10.016 | FL150 Roller |
| 44 | FL100.10.017 | Roller support /right |
| 45 | GB5782 | Bolt M12x90 |
| 46 | FL100.10.018 | Belt cover |
| 47 | GB11544 | V-Belt |